Critical Health & Safety Criteria for New Pools

(For initial Department of Health operating permit issuance)

Changes Tracked

- Source water quality acceptable

- Gravity drainage with collector tank (correctly sized for gpm)

- APSP Standard 16 drain cover(s) installed (aka VGB)

- Water velocity thru main drain < 1.5 feet per second

- Vacuum fitting(s) have spring loaded safety covers

- Slope break tile line and safety rope (where slope break requires this)

- Depth markers and NO diving markers correctly placed/sized

- Code listed equipment is NSF Std 50 approved, and chemicals added are NSF Std 60

- Filter size, filter type, flow rate and pump GPM per approved plans and code

- Interactive Water Feature (IWF) with full filtration & disinfection or validated UV disinfection

- Oxidation Reduction Potential (ORP) controllers on spas, wading pools & IWFs

- Automated pH controllers on spas, wading pools & IWFs

- Disinfectant application > 6 ppm (mg/L), or > 12 ppm, appropriate  for pool type

- Electrical interlock between recirculation pump and chemical feeders/generators

- Recirculation system water velocity per code (3, 6 and 10 ft/s)

- Pressure/vacuum gauges, flow meter (+ or – 10%) and valving per code

- Night use if applicable: Above water lights correct foot candle, engineer certified; UW light at correct 18” depth / wattage, LEDs must be lumen equivalent

- Pool size and turnover flowrate per code for type of use

- Minimum 15 foot wall to wall clearance

- Deck or curb handhold around perimeter <9” above skimmer opening midpoint

- Floor slope uniform and no greater than 1:10 or meets ADA 1:12

- Floor & wall color white or off-white, and non-slip

- Ladder structure, access and placement correct

- Handrails correctly placed over steps & anchored into bottom step/deck

- Intermediate steps uniform within ½ inch (treads and risers) with correct tile edges that are slip resistant

- Pool top and bottom step no more than 10 inch riser

- Benches/swimouts in correct location, sized, with correct tile edges that are slip resistant

- Wet deck surfaced correctly, slip resistant, and sloped to drain

- Restrooms < 200 feet, and food preparation > 12 feet from water

- No cross connections, maintain required air gap(s)

- Correct numbers of safety equipment (life ring + life hook) and Patron Safety Rules posted appropriately

- Approved water test kit provided